Applying Policy in the NSI environment

Status of This Document

Grid Forum Document (GFD), Recommendation (R).

Copyright Notice

Copyright © Open Grid Forum (2008-2015). All Rights Reserved.

Trademark

OGSA is a registered trademark and service mark of the Open Grid Forum.

Abstract

This document describes an approach to applying policy to the Network Services Interface (NSI) Connection Service protocol.

Contents

1.	Context and Overview	2

1.1	Network Services Interface	2

2.	Notational Conventions	2

3.	Summary	2

4.	Policy Requirements	3

5.	Policy enforcement	3

5.1	TREE Solution: Source Routing	4

5.2	CHAIN Solution: Source Routing	5

5.3	CHAIN Solution: hop-by-hop	6

6.	pathTrace Definition	8

6.1	PathType definition	8

6.2	SegmentType definition	9

6.3	StpType definition	10

6.4	Example	10

7.	Contributors	11

8.	Glossary	11

9.	Security Considerations	13

10.	Intellectual Property Statement	13

11.	Disclaimer	13

12.	Full Copyright Notice	13

13.	References	13

14.	Appendix A: Policy use cases	14

14.1	Link ownership	14

14.2	Transit policies	14

14.3	Link restrictive transit policies	15

14.4	Resource restrictive transit policies	15

14.5	Resource allocation policies	15

14.6	Preferred link policies	16

14.7	Selective reachability	17

15.	Appendix B: Schema extensions for pathTrace	17

# Context and Overview

## Network Services Interface

The Network Services Interface is a web service protocol that allows applications to monitor, control, interrogate, and support network resources that are made available by the provider of the network.  The NSI Connection Service deals specifically with the request and management of network Connections on transport networks.  NSI is inherently agnostic to the technology used in the transport plane.  This technology agnostic approach is built into the NSI topology representation and is supported through the use of Service Definitions.

A Connection Service can be requested by any application that has implemented an NSI CS requester agent. Similarly, any network provider who has implemented an NSI provider agent can service the request.

Each service is managed by an exchange of NSI messages between agents. These messages operate using a set of service primitives. Service primitives are the set of instructions that allow the requester to set up and manage a service. Each service request will result in the allocation of a service id for the new service instance.

This document describes how policy is applied to the NSI Connection Service.  This recommendation should be read in conjunction with GFD-R-212 Network Service Interface Connection Service version 2.0 [2], Open Grid forum GFD-I-213, Network Services Framework v2.0 [4] and NSI Authentication and Authorization [5].

# Notational Conventions

The keywords “MUST”, “MUST NOT”, “REQUIRED”, “SHALL”, “SHALL NOT”, “SHOULD”, “SHOULD NOT”, “RECOMMENDED”, “MAY”, and “OPTIONAL” are to be interpreted as described in [RFC 2119]. Words defined in the glossary are capitalized (e.g. Connection). NSI protocol messages and their attributes are written in camel case and italics (e.g. reserveConfirmed)

# Summary

Policy, in the context of this document, refers to the ability of a network provider to enforce acceptable usage policy in their local network. Network providers may apply policy rules that determine which users can request connectivity, how much bandwidth they can request or transit policies.  Network providers all implement some level of authorization policy in their networks.  This document describes an NSI CS policy framework that defines how the NSI CS protocol is used to provide sufficient information to the provider to allow them to understand the originator of the request and the routing details.  The provider is then able to apply local policy in their network based on this information.

This document is organized into three main sections as follows.

- Section 4 ‘Policy Requirements’ is a formal statement of the requirements in NSI that allows providers to enforce policy.  This section is normative.

- Section 5 ‘Policy enforcement’ describes how policy can be enforced in the NSI CS. This section is normative.

- Section 6 ‘pathTrace ’ describes the pathTrace extensions to the NSI CS v2.0 schema and how it should be used.   This section is normative.

Appendix A describes the research and education community use-cases for policy.  Appendix B contains the pathTrace extensions to the NSI CS v2.0 schema. This section is normative.

# Policy Requirements

The examples of policy-based routing decisions described in the previous section introduce new requirements for path finding and the process by which local policy is enforced:

A mechanism MUST be supported in the NSI CS protocol so that a uPA associated with any Network understands the proposed end-to-end path so that it can make a decision on whether to approve the local reservation segment.

Where a reservation is rejected for policy reasons, there MUST be a mechanism to report this back to the uRA so that it can terminate the full end-to end reservation.

The NSI CS policy framework MUST assume that the responsibility for terminating Connections is held with the uRA, this allows the uRA to make decisions on what to do under the failure scenario.

Where a reservation is rejected for policy reasons, there MUST be a mechanism to provide information back to the requester about the reason for the rejection so that the requester can try alternative Connection requests.

The NSI CS policy framework MUST use the existing NSI protocol and behaviors where possible to reduce protocol churn and will incorporate the solution in the existing NSI protocol framework.

The NSI CS policy framework MUST assume that in TREE mode, full inter-network path resolution can be performed at the root aggregator and source base routing MUST be used.  The full path MUST be resolved by the aggregator before the path is sent down the TREE.  This will ensure that full information is available so that policy can be applied locally by each Network.

The NSI CS policy framework MUST assume that in the CHAIN mode either source or hop-by-hop routing can be performed.

Network routing policy information MUST be made available to pathfinders for more effective route resolution.

The NSI CS policy framework MUST assume that the act of holding resources associated with a reservation could be done without approval, but the committing of a reservation will not occur without all uPA.path segments having confirmed that the reservation meets local policy

The NSI CS policy framework MUST assume that the service plane is trusted and that the NSA will behave correctly in the context of the NSI protocol.

# Policy enforcement

This section describes how policy is enforced in the NSI Connection Service.   This mechanism makes use of the inherent Service Plane trust between NSA along with proper operation of the NSI protocol to allow for uPA enforcement of connection path related policies.  At the base of the mechanism is the definition of a new NSI message header element containing the detailed Connection path proposed for the reservation.  This new path trace information is propagated to each uPA involved in the connection as part of the NSI reserve message flow, allowing the uPA to evaluate the full reservation path against local routing policy as part of the resource reserving phase.  A policy failure at the uPA is communicated using the standard reserveFailed message, resulting in no changes to the core NSI CS protocol.

## TREE Solution: Source Routing

This section describes how policy is implemented in the case of “source routing” for a TREE signaled Connection reservation.  The NSI models for signaling and pathfinding are documented in detail in the NSI informational document GFD.217 Network Service Interface Signaling and Path Finding [6].

As shown in Figure 1, a uRA creates the initial reserve message and sends it to an AG NSA that will act as the top-level root for this reservation.  The root AG NSA will resolve the full path for the reservation using any policy information that it has access to.  Note that NSI does not define a policy distribution mechanisms, the method used to distribute policy is up to the implementer.

Reserve messages are created for individual path segments with the fully resolved path stored in the NSI message header along with the root AG’s NSA identifier.  The root AG then routes these individual reservation messages to the target NSA for each segment using the Service Plane.

Any subsequent AG NSAs receiving a reserve request for a Connection can see the full end-to-end path in the header, and does not need to perform any further path finding (unless it is a special NSA hiding networks behind it), and will pass the reserve request to the next hop NSAs down the TREE until the leaf uPAs involved in the Connection are reached.  At each hop the NSA has to re-formulate the reserve request - a complete new reservation message is created but with same source destination etc.

A uPA receives the reserve request and uses the full path information in the NSI message header to determine if the request meets local policy requirements.

- If the proposed path violates any local policy, a reserveFailed message is returned with the appropriate serviceException information.  The reserveFailed message is sent up the TREE where corrective action can be taken by an upstream AG, or ultimately propagate the failure through to the uRA.

- If the proposed path passes all policies, and the reservation criteria can be met, resources are held and a reserveConfirmed message is returned as per existing protocol definition. The reserveConfirmed message is sent up the TREE to the root AG.

If a policy was violated, the root AG will inform the uRA of the reservation failure due to a policy error, and the uRA can abort the reservation as per the standard, OR the root AG can take corrective action itself, aborting the existing path segments, and using the learned policy information to compute an alternative path.

Figure 1 - TREE source routing reserve message flow.

## CHAIN Solution: Source Routing

This section describes how policy is implemented in the case of “source routing” for a CHAIN signaled Connection reservation.  The NSI models for signaling and path finding are documented in detail in the NSI informational document GFD.217 Network Service Interface Signaling and Path Finding [6].  In the CHAIN solution each NSA associated with network resources is both an AG and uPA, with the AG capable of performing path finding and message forwarding, and the uPA managing associated network resources.  For the purpose of this description we use the term NSA as the combined AG/uPA capabilities, and uRA for the standard initiator of the reservation request.

As shown in Figure 2, a uRA creates the initial reserve message and sends it to the head end NSA for the CHAIN that will act as the root for this reservation (this is the NSA associated with the network of the source STP).  The head-end NSA then resolves the full path for the reservation using any policy information that it has access to.  Note that the mechanism for distribution of policy between Networks is out-of-scope of this recommendation.

A Reserve message is created by the head-end NSA, adding the ERO for the fully resolved path through the transport plane.  In addition, the detailed path is also stored in the NSI header (tagged as type source routing) along with the head-end NSA identifier for use by policy enforcement.  The head-end NSA, after validating any local polices and securing associated resources, routes this reserve message to the adjacent NSA along the Transport Plane of this connection path.

The next hop NSA receives the reserve request and uses the full path information in the header to determine if the request meets local policy requirements.

- If the proposed path violates any local policy, a reserveFailed message is returned with the appropriate serviceException information.  The reserveFailed message is sent back up the CHAIN to the head-end NSA.

- If the proposed path passes all policies, and the reservation criteria can be met, resources are held and a reserve message is send to the next NSA along the CHAIN.

- If this was the tail end NSA then a reserveConfirmed message is returned. The reserveConfirmed message is sent back up the CHAIN to the head-end NSA.

If a policy was violated, the head-end NSA will inform the uRA of the reservation failure due to policy error, and the uRA can abort the reservation as per the standard.  or the head-end NSA can take corrective action itself, aborting the existing path segments, and using the local Network policy learnt using trial-and-error approach to compute an alternative path.

Figure 2 - CHAIN source-routing reserve message flow.

## CHAIN Solution: hop-by-hop

This section describes how policy is implemented for the case of “hop-by-hop” routing for a CHAIN signaled Connection reservation.  The NSI models for signaling and pathfinding are documented in detail in the NSI informational document  GFD.217 Network Service Interface Signaling and Path Finding [6].  Similar to the previous CHAIN section, we use the term NSA as the combined AG/uPA capabilities, and uRA for the standard initiator of the reservation request.

A uRA creates the initial reserve message and sends it to the head end NSA for the CHAIN that will act as the root for this reservation (this is the NSA associated with the network of the source STP).  The hop-by-hop routing solution functions similar to the CHAIN-based source routing solution except that the complete path a reservation takes is not known until the tail end NSA is reached.  As the reserve request propagates from source network to destination network:

- Hop-by-hop routing (distance vectors, etc.) is used to determine the outgoing SDP in each Network.

- The NSA holds local network resources associated with the reservation.

- The proposed local path segment is added to the NSI header and the reserve is propagated to the next peer NSA in the CHAIN.

- An early fail can occur (based on policy violation of the computed path so far) if the computed path up to this point violates any policies within the NSA, and a reserveFailed message is returned to the adjacent upstream peer.

When the tail end NSA in the destination network is reached:

- The NSA resolves the local path segment and holds associated resources (if available).

- The NSA adds the local path segment to the existing path taken from the header to complete the full path.

- The NSA evaluates local policies of the destination Network against the full computed path, and if valid from its perspective, returns the full path in the NSI header of the reserverConfirmed to the adjacent upstream peer.

- If the proposed path violates any policy, a reserveFailed message is returned with appropriate serviceException information.

As the reserveConfirmed messages propagate back from destination to source, each Network performs an evaluation of its local policies against the full path within the NSI header before issuing a reserveConfirmed to the next upstream peer.

At any point if an NSA fails policy evaluation, a reserveFailed is generated thereby failing the reservation as per standard protocol behaviors.

Once the head-end NSA has validated its local policies based on the final path, a reserveConfirmed can be returned to the originating uRA.

Figure 3 – CHAIN hop-by-hop routing reserve message flow.

# pathTrace Definition

To help facilitate the communication of path trace information within the NSI reserve message exchange we introduce a new schema element called “pathTrace” into the NSI Header element.

Figure 4 – The pathTrace element.

The pathTrace element contains the following parameters:

| Parameter | Type | M/O | Description |
| --- | --- | --- | --- |
| id | Attr | M | In the case of TREE, this attribute contains the NSA identifier of the aggregator that performed path resolution, while for CHAIN, it is the identifier of the first (head-end) NSA allocating transport plane resources. This identifier is added for traceability back to the NSA performing initial path resolution. |
| type | Attr | M | Identifies the type of routing performed for this path allocation. If type is set to "source" then the full end-to-end path was computed at the root NSA of the reservation and included in the reserve request. If type is set to “hop-by-hop” then the full path will be built as the reserve request propagates through the network. |
| connectionId | Elem | M | The connection identifier for the reservation in the context of the NSA identified by the id attribute. This identifier is added for traceability to the originating reservation associated with this path. |
| path | Elem | M | In the case of a "source" routing the NSA doing path resolution includes the complete path, while for “hop-by-hop” each NSA allocating data plane resources adds its path segment on the outbound reserve request until the full path is completed by the tail end NSA. This path element is used by uPA to perform routing policy enforcement. |

## PathType definition

PathType is a type definition for path information within the path trace element.  A path consists of a sequence of individual path segments.

Figure 5 – The PathType definition.

The PathType structure contains the following parameters:

| Parameter | Type | M/O | Description |
| --- | --- | --- | --- |
| segment | Elem | M | One of more segment elements in the overall connection path. |

## SegmentType definition

SegmentType is a type definition for an individual path segment within the overall connection path.  This represents the connection segment for a single domain.

Figure 6 – The SegmentType definition.

The SegmentType structure contains the following parameters:

| Parameter | Type | M/O | Description |
| --- | --- | --- | --- |
| id | Attr | M | The NSA identifier associated with this path segment. |
| order | Attr | M | The sequence order of the connection in the overall path. As new segments are added to the path trace this value is increased by one over the last added segment. |
| stp | Elem | M | A list of STP identifier within this domain that are part of the overall path ordered by their sequence within the connection. This list will usually only contain ingress and egress STP, however, more flexibility is provided to model internal STP as well. |

## StpType definition

An extended type definition for an STP identifier that includes ordering capabilities.  This type extends from the based point-to-point service type’s StpIdType definition (a simple string valued type) to include an order attribute.

Figure 7 – The StpType definition.

The StpType structure contains the following parameters:

| Parameter | Type | M/O | Description |
| --- | --- | --- | --- |
| order | Attr | M | The order of this STP within a sequence of STP. |

## Example

The following is path trace example for a connection with three segments running through networks “Aruba”, “Curacao”, and “Bonaire”.  In this example, the user requests a reservation from “stpA” in network Aruba through to “stpZ” in network Bonaire using the Grenada uRA “urn:ogf:network:grenada.net:2013:nsa-requester”.

The Grenada uRA NSA creates an NSI reserve message with the requested reservation criteria and passes it on to the associated aggregator NSA “urn:ogf:network:grenada.net:2013:nsa-aggr” for processing.  The AG receives the NSI reserve message and performs path finding.  The path shown below in Figure 8 is computed { (stpA, toCuracao), (toAruba, toBonaire), (toCuracao, stpZ) }.

Figure 8 – Example network for pathTrace.

The AG now creates a pathTrace element to include in the NSI message header.  The AG populates pathTrace.id attribute with its own NSA identifier as the NSA performing path finding.  It also sets the pathTrace.type attribute to “source” routing identifying that the complete path has been supplied, and populates the local connectionId associated with the reservation in the pathTrace.connectionId element for the purpose of traceability.  Finally, the AG populates the pathTrace.path element with the detailed path ordered from source to destination, including the individual uPA NSA identifier in the path.id attribute for each of the segments.

For this example the AG would generate the following pathTrace element:

<tns:pathTrace id="urn:ogf:network:grenada.net:2013:nsa-aggr" type="source"
        xmlns:tns="http://schemas.ogf.org/nsi/2015/04/connection/pathtrace">
    <connectionId>urn:uuid:59d6c0b2-a8e0-4583-ae8a-0fc84eb89f07</connectionId>
    <path>
        <segment id="urn:ogf:network:aruba.net:2013:nsa" order="0">
            <stp order="0">urn:ogf:network:aruba.net:2013::stpA?vlan=1790</stp>
            <stp order="1">urn:ogf:network:aruba.net:2013::toCuracao?vlan=1790</stp>
        </segment>
        <segment id="urn:ogf:network:curacao.net:2013:nsa" order="1">
            <stp order="0">urn:ogf:network:curacao.net:2013::toAruba?vlan=1790</stp>
            <stp order="1">urn:ogf:network:curacao.net:2013::toBonaire?vlan=1790</stp>
        </segment>
        <segment id="urn:ogf:network:bonaire.net:2013:nsa" order="2">
            <stp order="0">urn:ogf:network:bonaire.net:2013::toCuracao?vlan=1790</stp>
            <stp order="1">urn:ogf:network:bonaire.net:2013::stpZ?vlan=1790</stp>
        </segment>
    </path>
</tns:pathTrace>

# Contributors

Chin Guok, ESnet

Tomohiro Kudoh, AIST

John MacAuley, ESnet

Guy Roberts, GEANT

Henrik Thostrup Jensen, NORDUnet

Hans Trompert, SURFnet

# Glossary

| Aggregator (AG) The Aggregator is an NSA that has more than one child NSA, and has the responsibility of aggregating the responses from each child NSA. Connection A Connection is an NSI construct that identifies the physical instance of a circuit in the Transport Plane. A Connection has a set of properties (for instance, Connection identifier, ingress and egress STPs, capacity, or start time). Connections can be either unidirectional or bidirectional. Connection Service (CS) The NSI Connection Service is a service that allows an RA to request and manage a Connection from a PA. Control and Management Planes The Control Plane and/or Management Plane are not defined in this document, but follow common usage. Discovery Service The NSI discovery service is a web service that allows an RA to discover information about the services available in a PA and the versions of these services. Edge Point A network resource that resides at the boundary of an intra-network topology, this may include for example a connector on a distribution frame, a port on an Ethernet switch, or a connector at the end of a fiber ero An Explicit Routing Object (ero) is a parameter in a Connection request. It is an ordered list of STP constraints to be used by the inter-Network pathfinder. Inter-Network Topology This is a topological description of a set of Networks and their transfer functions, and the connectivity between Networks. Network A Network is an Inter-Network topology object that describes a set of STPs with a Transfer Function between STPs. Network Markup Language (NML) The Network Markup Language is an XML based network resource description language developed in the OGF. Network Resource Manager (NRM) The Network Resource Manager is the entity that manages a network, typically this will be the equipment vendor’s network management system. Network Services Network Services are the full set of services offered by an NSA. Each NSA will support one or more Network Services. Network Service Agent (NSA) The Network Service Agent is a concrete piece of software that sends and receives NSI Messages. The NSA includes a set of capabilities that allow Network Services to be delivered. Network Services Framework (NSF) The Network Services framework describes an NSI message-based platform capable of supporting a suite of Network Services such as the Connection Service and the Topology Service. Network Service Interface (NSI) The NSI is the interface between RAs and PAs. The NSI defines a set of interactions or transactions between these NSAs to realize a Network Service. NSI Message An NSI Message is a structured unit of data sent between an RA and a PA. NSI Topology The NSI Topology defines a standard ontology and a schema to describe network resources that are managed to create the NSI service. The NSI Topology as used by the NSI CS (and in future other NSI services) is described in: GWD-R-P: Network Service Interface Topology Representation [3]. Open Grid Forum (OGF) The OGF is the Standards Developing Organization (SDO) that is home to the NSI Standards. Provision Provisioning is the process of requesting the creation of the physical instance of a Connection in the data plane. Requester/Provider Agent (RA/PA) An NSA acts in one of two possible roles relative to a particular instance of an NSI. When an NSA requests a service, it is called a Requester Agent (RA). When an NSA realizes a service, it is called a Provider Agent (PA). A particular NSA may act in different roles at different interfaces. Service Demarcation Point (SDP) Service Demarcation Points (SDPs) are NSI topology objects that identify a grouping of two Edge Points at the boundary between two Networks. Service Termination Point (STP) Service Termination Points (STPs) are NSI topology objects that identify the Edge Points of a Network in the intra-network topology. Service Plane The Service Plane is a plane in which services are requested and managed; these services include the Network Service. The Service Plane contains a set of Network Service Agents communicating using Network Service Interfaces. Reserve When a Provider Agent receives (and then confirms) a Connection Reservation request the Provider Agent then holds the resources needed by the Connection. Terminate Terminating is the process which will completely remove a Reservation and Release any associated Connections. This term has a formal definition in the CS state-machine. Topology Distribution Service The NSI Topology distribution Service is a service that allows the NSI topology to be exchanged between NSAs. Transport Plane The Transport Plane refers to the infrastructure that carries the physical instance of the Connection, e.g. the Ethernet switches that deliver the circuit. Ultimate PA (uPA) The ultimate PA is a Provider Agent that has an associated NRM. Ultimate RA (uRA) The ultimate RA is a Requester Agent is the originator of a service request. XML Schema Definition (XSD) XSD is a schema language for XML. eXtensible Markup Language (XML) XML is a markup language that defines a set of rules for encoding documents in a format that is both human-readable and machine-readable. |  |
| --- | --- |

# Security Considerations

Security considerations are dealt with in Open Grid forum GWD-R draft-trompert-gwdi-nsi-aa-v04, NSI Authentication and Authorization [5].

No additional security issues have been raised.

# Intellectual Property Statement

The OGF takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this specification can be obtained from the OGF Secretariat.

The OGF invites any interested party to bring to its attention any copyrights, patents or patent applications, or other proprietary rights which may cover technology that may be required to practice this recommendation. Please address the information to the OGF Executive Director.

# Disclaimer

This document and the information contained herein is provided on an “As Is” basis and the OGF disclaims all warranties, express or implied, including but not limited to any warranty that the use of the information herein will not infringe any rights or any implied warranties of merchantability or fitness for a particular purpose.

# Full Copyright Notice

Copyright (C) Open Grid Forum (2008–2015). All Rights Reserved.

This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this paragraph are included on all such copies and derivative works. However, this document itself may not be modified in any way, such as by removing the copyright notice or references to the OGF or other organizations, except as needed for the purpose of developing Grid Recommendations in which case the procedures for copyrights defined in the OGF Document process must be followed, or as required to translate it into languages other than English.

The limited permissions granted above are perpetual and will not be revoked by the OGF or its successors or assignees.

# References

- ITU-T, G.805: Generic functional architecture of transport networks

- Open Grid forum GFD.212 Network Service Interface Connection Service, v2.0

- IETF RFC 4655, "A Path Computation Element (PCE)-Based Architecture",
http://www.rfc-editor.org/rfc/rfc4655.txt

- Open Grid forum GFD.213, Network Services Framework v2.0, http://www.ogf.org/documents/GFD.213.pdf

- Open Grid forum GWD-R draft-trompert-gwdi-nsi-aa-v04, NSI Authentication and Authorization, https://redmine.ogf.org/dmsf_files/13398?download=

- Open Grid forum GFD.217 Network Service Interface Signaling and Path Finding https://www.ogf.org/documents/GFD.217.pdf

# Appendix A: Policy use cases

This section lists policy requirements that have been identified by network providers that wish to implement the NSI CS protocol in their network.

## Link ownership

In some situations a network’s demarcation point extends beyond the edge of their network to include the link that connects to the far end network.  In Figure 9 below we see Link A is owned by Network A and Link B is owned by Network B.

Figure 9 Link ownership

In this case, the Exchange X should not be able to initiate a Connection on port X.A without the approval of Network A, and similarly, it should not initiate a Connection on port X.B without the approval of Network B.  If Exchange X was to make a Connection between port X.A to X.B without the explicit consent from either Networks A and B, this could block bandwidth in Networks A and B, constituting a denial of service attack.  The NSI policy framework should include a mechanism that would allow policy to be instituted in Exchange X to prevent this.

## Transit policies

NSI CS transit policies may be applied by the Network to determine what traffic may transit based on source and/or destination Network of a Connection.  For example in Figure 10, Network A may apply a local policy allowing Network networks A1-A3 to connect to each other and to the networks B and C without restriction while preventing transit connections between Network B and C.

Figure 10 Transit policies

## Link restrictive transit policies

NSI CS policy may be applied on a link restriction basis.  In Figure 11 below, Exchange X has a local policy that allows traffic between Network A and Network C via Links A and C1, but not using Links A, B, and C2.

Figure 11 Link restrictive transit policies

## Resource restrictive transit policies

An example of a resource based transit policy is shown in Figure 12 below.  In this case Exchange X allows a maximum bandwidth between Network A and Network C independent of the path.

Figure 12 Resource restrictive transit policies

## Resource allocation policies

NSI CS policy can be used to restrict the path a Connection may take through the network based on the segmentation of allocated resources within the network to specific groups of users.  In the example Figure 13 below, Link C1 is tagged for use by user group 1 only, while all other links are tagged for cooperative sharing.  Only users that are members of group 1 may use link C1 in reservation requests.

Figure 13 Resource allocation policies

## Preferred link policies

NSI CS policy can be used to prefer one link to another.  In Figure 14 below, due to transit policies within Network C, transit traffic from Network A to Network D should use preferred Link D1 until capacity is consumed, while transit traffic between Network B and Network D should use preferred Link D2.

Figure 14 Preferred link policies

In the situation depicted below in Figure 15, there are two equal distant paths between Network A and Network D; however, Network A has a preferred link policy such that any traffic between Network A and D must transit Network C via Link AC, the preferred route.

Figure 15 Preferred path policies

## Selective reachability

This type of policy restricts the traffic that can terminate in a network, along with transit rules for associated traffic

- A should be able to reach B+D

- B should be able reach all.

- C should be able to reach B+D

- D should be able to reach A+B+C.

That is, A and C are not exchanging traffic, but C provides transit to D, and D has transit to A through B and C

Figure 16 Selective reachability

# Appendix B: Schema extensions for pathTrace

<?xml version="1.0" encoding="UTF-8"?>
<!--
    The OGF takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights.  Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this specification can be obtained from the OGF Secretariat.
    
    The OGF invites any interested party to bring to its attention any copyrights, patents or patent applications, or other proprietary rights which may cover technology that may be required to practice this recommendation.  Please address the information to the OGF Executive Director.
    
    This document and the information contained herein is provided on an "As Is" basis and the OGF disclaims all warranties, express or implied, including but not limited to any warranty that the use of the information herein will not infringe any rights or any implied warranties of merchantability or fitness for a particular purpose.
    
    Copyright (C) Open Grid Forum (2009-2015). All Rights Reserved.
    
    This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this paragraph are included on all such copies and derivative works. However, this document itself may not be modified in any way, such as by removing the copyright notice or references to the OGF or other organizations, except as needed for the purpose of developing Grid Recommendations in which case the procedures for copyrights defined in the OGF Document process must be followed, or as required to translate it into languages other than English.
    
    The limited permissions granted above are perpetual and will not be revoked by the OGF or its successors or assignees.
    
    Open Grid Forum NSI Connection Services Protocol v2.0 - Path trace extensions.
-->
<xsd:schema targetNamespace="http://schemas.ogf.org/nsi/2015/04/connection/pathtrace"
    xmlns:xsd="http://www.w3.org/2001/XMLSchema"
    xmlns:types="http://schemas.ogf.org/nsi/2013/12/services/types"
    xmlns:ftypes="http://schemas.ogf.org/nsi/2013/12/framework/types"
    xmlns:tns="http://schemas.ogf.org/nsi/2015/04/connection/pathtrace">
    
    <xsd:annotation>
        <xsd:appinfo>OGF NSI CS Path Trace 2015-04-30</xsd:appinfo>
        <xsd:documentation xml:lang="en">
            This is an XML schema document describing the path trace extension
            to the OGF NSI Connection Services protocol version 2.0.  This 
            defines a new header element used to model the full path of a
            reservation.
        </xsd:documentation>
    </xsd:annotation>
    
    <!-- Import the common NSI framework types. -->
    <xsd:import namespace="http://schemas.ogf.org/nsi/2013/12/framework/types"
        schemaLocation="ogf_nsi_framework_types_v2_0.xsd"/>
    
    <!-- Import the common NSI service types. -->
    <xsd:import namespace="http://schemas.ogf.org/nsi/2013/12/services/types"
        schemaLocation="ogf_nsi_services_types_v2_0.xsd"/>

    <xsd:element name="pathTrace" type="tns:PathTraceType">
        <xsd:annotation>
            <xsd:documentation xml:lang="en">
                The header element modeling a connection path through the network.
            </xsd:documentation>
        </xsd:annotation>     
    </xsd:element>

    <xsd:complexType name="PathTraceType">
        <xsd:annotation>
            <xsd:documentation xml:lang="en">
                Type definition for the path trace information.
                
                Attributes:
                
                id - In the case of TREE, this attribute contains the NSA
                identifier of the aggregator that performed path resolution,
                while for CHAIN, it is the identifier of the first (head-end)
                NSA allocating transport plane resources.  This identifier is
                added for traceability back to the NSA performing initial
                path resolution.
                
                type - Identifies the type of routing performed for this path
                allocation.  If type is set to "source" then the full end-to-end
                path was computed at the root NSA of the reservation and
                included in the reserve request.  If type is set to “hop-by-hop”
                then the full path will be built as the reserve request
                propagates through the network.
                
                Elements:

                connectionId - Connection identifier for the reservation in the
                context of the NSA identified by the "id" attribute.  This
                identifier is added for traceability to the originating reservation
                associated with this path.
                
                path - In the case of a "source" routing the NSA doing path
                resolution includes the complete path, while for “hop-by-hop”
                each NSA allocating data plane resources adds its path
                segment on the outbound reserve request until the full path is
                completed by the tail end NSA.  This path element is used by
                uPA to perform routing policy enforcement.
            </xsd:documentation>
        </xsd:annotation>
        <xsd:sequence>
            <xsd:element name="connectionId" type="ftypes:ConnectionIdType" />
            <xsd:element name="path" type="tns:PathType" maxOccurs="unbounded" />
        </xsd:sequence>
        <xsd:attribute   name="id" type="ftypes:NsaIdType" use="required" />
        <xsd:attribute   name="type" type="tns:RoutingType"  use="required" />
    </xsd:complexType>
    
    <xsd:complexType name="PathType">
        <xsd:annotation>
            <xsd:documentation xml:lang="en">
                Type definition for path information within the trace. A path
                consist of a sequence of path segments.
                
                Elements:
                
                segment - A single segment in the overall connection path.
            </xsd:documentation>
        </xsd:annotation>
        <xsd:sequence>
            <xsd:element name="segment"   type="tns:SegmentType" maxOccurs="unbounded" />
        </xsd:sequence>
    </xsd:complexType>
    
    <xsd:complexType name="SegmentType">
        <xsd:annotation>
            <xsd:documentation xml:lang="en">
                Type definition for a path segment within the overall
                connection path.  This represents the connection segment for a
                single domain.
                
                Attributes:
                
                id - The NSA identifier associated with this path segment.
                
                order - The sequence order of the connection in the overall
                path.  As new segments are added to the path trace this value
                is increased by one over the last added segment.
                
                Elements:
                
                stp - A list of STP identifier within this domain that are part
                of the overall path ordered by their sequence within the
                connection.  This list will usually only contain an ingress and
                egress STP, however, more flexibility is provided to model
                internal STP as well.
            </xsd:documentation>
        </xsd:annotation>
        <xsd:sequence>
            <xsd:element name="stp"  type="tns:StpType" maxOccurs="unbounded" />
        </xsd:sequence>
        <xsd:attribute   name="id"    type="ftypes:NsaIdType" use="required" />
        <xsd:attribute   name="order" type="xsd:int" use="required" />
    </xsd:complexType>
    
    <xsd:complexType name="StpType">
        <xsd:annotation>
            <xsd:documentation xml:lang="en">
                An extended type definition for an STP identifier that includes
                ordering capabilities.
                
                Attributes:
                
                order - The order of this STP within a sequence of STP.
            </xsd:documentation>
        </xsd:annotation>
        <xsd:simpleContent>
            <xsd:extension  base="types:StpIdType">
                <xsd:attribute  name="order"  type="xsd:int"  use="required"/>
            </xsd:extension>
        </xsd:simpleContent>
    </xsd:complexType>
    
    <xsd:simpleType name="RoutingType">
        <xsd:annotation>
            <xsd:documentation xml:lang="en">
                Type definition enumerating the types of routing supported by
                the path trace.
            </xsd:documentation>
        </xsd:annotation>
        <xsd:restriction base="xsd:string">
            <xsd:enumeration value="source" />
            <xsd:enumeration value="hop-by-hop" />
        </xsd:restriction>
    </xsd:simpleType>
</xsd:schema>

# Comments

I assume these are normative.

It is not clear why this is stated.

In fact the rest of the doc describes how policy checking is done for a reserve – e.g. see next section.

Need to review this requirement

At the base of the mechanism …

Reference Fig 1

… created but with the same …

I believe the message goes via a ladder of the next higher AGs and then to the root AG

NOT direct from a uPA to the root AG.

Yes, your assumption is correct.  This is implied in the expression ‘sent up the TREE’

Reference Fig 2

returned

The figure has “up”.

Previous paras go “down” to the uPA

I suggest it is consistent

up

Does “OR” have special meaning?

Please update the reference

document GFD.217 Network Service Interface Signaling and Path Finding [6].

returned

… and to the networks B and C …

The Grey dashed line on Link D2 should go to Network B not network A